## Slide 1
Notes: <number>

## Slide 4
Any biological sample may be infectious and therefore presents a hazard to -any person handling
-during collection
-during transport
-during opening and proceeding

## Slide 5
Risk Group 1 (no or low individual and community risk)
A microorganism that is unlikely to cause human or animal disease.
Risk Group 2 (moderate individual risk, low community risk)
A pathogen that can cause human or animal disease but is unlikely to be a serious hazard to laboratory workers, the community, livestock or the environment. Laboratory exposures may cause serious infection, but effective treatment and preventive measures are available and the risk of spread of infection is limited.
Risk Group 3 (high individual risk, low community risk)
A pathogen that usually causes serious human or animal disease but does not ordinarily spread from one infected individual to another. Effective treatment and preventive measures are available.
Risk Group 4 (high individual and community risk)
A pathogen that usually causes serious human or animal disease and that can be readily transmitted from one individual to another, directly or indirectly. Effective treatment and preventive measures are not usually available.
Notes: <number>

## Slide 7
in a BSL1 laboratory are unlikely to cause disease in healthy adults and pose a low level of risk to the community, most of the microorganisms used in the microbiology teaching laboratory are capable of causing an infection given the appropriate circumstances. Many best practices should be adopted to minimize the risk of laboratory-acquired infections and to train students in the proper handling of microorganisms.

## Slide 10
Personal Protection Requirements
 Wear safety goggles or glasses when handling liquid cultures, when performing procedures that may create a splash hazard, or when spread plating.
 Wear closed-toed shoes.
 Wear gloves when handling microorganisms or hazardous chemicals.
 Recommended: Wear lab coats.
Notes: <number>

## Slide 11
Lab Physical Space Requirements
 Require all lab space to include:
o Nonporous floor, bench tops, chairs, and stools.
o Sink for hand washing.
o Eyewash station.
o Lockable door to the room.
 Recommended: Keep personal belongings in an area separate from the work area.
 Recommended: Use a working and validated autoclave.
Notes: <number>

## Slide 12
Standard Lab Practices
 Wash hands before and after the lab session.
 Tie back long hair.
 Disinfect bench before and after the lab session with a disinfectant known to kill the organisms handled
 Use disinfectants according to manufacturer instructions.
 Do not bring food, gum, drinks (including water), or water bottles into the lab.
 Do not touch the face, apply cosmetics, adjust contact lenses, or bite nails.
 Do not handle personal items (cosmetics, cell phones, calculators, pens, pencils, etc.) while in the lab.
 Do not mouth pipette.
 Label all containers clearly.
 Keep door closed while the lab is in session. Lab director or instructor approves all personnel entering the lab.
 Minimize the use of sharps. Use needles and scalpels according to appropriate guidelines and precautions
Notes: <number>

## Slide 13
Use proper transport vessels (test tube racks) in the lab, and store these in a leak-proof container when work with them is complete.
 Use leak-proof containers for storage and transport of infectious materials.
 Use microincinerators or disposable loops rather than Bunsen burners whenever possible.
 Use appropriate pest-control methods for rodents, insects, etc.
 Arrange for proper (safe) decontamination and disposal of contaminated material (e.g., in a properly maintained and validated autoclave) or arrange for licensed waste removal in accordance with local, state, and federal guidelines.
 Do not handle broken glass with fingers; use a dustpan and broom.
 Notify instructor of all spills or injuries.
 Document all injuries according to school, university, or college policy.
 Use only institution-provided marking pens and writing instruments.
 Teach, practice, and enforce the proper wearing and use of gloves.
 Require immune-compromised students (including those who are pregnant or may become pregnant) and students living with or caring for an immune-compromised individual to consult physicians to determine the appropriate level of participation in the lab.
 Recommended: Keep note-taking and discussion practices separate from work with hazardous or infectious material
Notes: <number>

## Slide 14
Notes: <number>

## Slide 15
BSL2 is suitable for organisms that pose moderate individual risk and low community risk for infection. When good microbiological techniques are used, these organisms rarely cause serious disease, and effective treatment for laboratory-acquired infections is available. Best practices must be adopted to minimize the risk of laboratory-acquired infections and to train students in the proper handling of organisms that require BSL2 procedures. Students should always demonstrate proficiency in laboratory techniques using organisms that require BSL1 practices before being allowed to handle organisms that require BSL2 practices.
Notes: <number>

## Slide 17
        Personal Protective Equipment
Safety goggles or glasses when handling liquids or when plating
Lab coats
Closed-toed shoes
Gloves when handling hazardous and/or infectious materials.
Nonporous Lab Furniture
Culture Preservation
    Note-Taking Area
Disinfectants
Routine benchtop disinfection
Biological Spills
Notes: <number>

## Slide 18
  • Wear gloves and lab coat.
Use forceps to pick up broken glass and discard into sharps container.
• Cover spilled material with paper towels.
• Add diluted disinfectant in sufficient quantity to ensure effective microbial inactivation.
• Allow a 30-minute contact for disinfection.
• Dispose of towels in biohazard waste container.
• Wipe spill area with diluted disinfectant.
• Wash hands with soap and water when finished.

## Slide 22
work with indigenous or exotic agents with potential for respiratory transmission or lethal consequences.
Examples:
  M. tuberculosis,
  B. anthracis

## Slide 24
Biosafety Level 4:
Level 4 facilities are designed for work with dangerous and exotic agents, which pose a high risk to individuals to contact a life-threatening disease. In these facilities, all manipulations are considered to be of high risk, and the procedures and safety equipment are designed to prevent exposure.
BSL 4: lethal exotic agents especially where there is no vaccine or therapy.
  BSL 4 facility is separate facility
  Examples: Ebola, Marburg and Lassa Fever viruses

## Slide 25
Fire
Bunsen Burners
Autoclaves
Compressed Gas Cylinders
Broken Glassware
Razorblades and needles
Electrical Equipment
Ultraviolet light
Notes: <number>

## Slide 26
Flammable Chemicals
Reactive Chemicals
Corrosive Chemicals
Toxic Chemicals
Notes: <number>